## Slide 1: Edge AI for Personalized Healthcare Wearable Tremor Detection for Early Parkinson’s

## Slide 2: 1. Project Overview
Goal: Detect Parkinson’s rest tremor (4–6 Hz) using wearable motion sensors
Early detection of Parkinson’s Disease (PD) remains a major challenge because diagnosis typically happens only after noticeable motor symptoms appear. One of the earliest and most reliable biomarkers is rest tremor, which typically occurs in the 4–6 Hz frequency band. This project builds an Edge AI–powered wearable/phone-based tremor detection system using IMU motion sensors (accelerometer & gyroscope) and Edge Impulse Studio to detect subtle tremor patterns during resting conditions.
The goal is to enable low-cost, real-time, continuous monitoring of early Parkinson’s symptoms—without requiring hospital visits, lab equipment, or cloud servers. By leveraging Edge AI, all detection happens locally on the device, ensuring privacy, speed, and low energy consumption.
This project falls under the Model Development Track, focusing on dataset quality, model accuracy, and efficient Edge deployment.

## Slide 3: 2. Motivation & Impact
⭐ Motivation
Parkinson’s Disease affects millions, and one of its early clinical indicators is rest tremor frequency (typically 3–7 Hz).
Traditional tremor analysis requires clinical equipment, which is expensive and not accessible for everyone.
There is a need for a low-cost, real-time, mobile-based approach to analyze tremor patterns.
By using Edge Impulse, we can process and classify tremor signals directly on edge devices like smartphones and microcontrollers.
This project makes early detection and monitoring more accessible, portable, and affordable.
⭐ Impact
Early Identification Helps clinicians and patients detect abnormal tremor frequencies early and track disease progression.
Real-Time Monitoring The system runs locally on a device—no internet needed—giving instant feedback.
Low Cost & Scalable Works with phones or simple sensors like accelerometers, making it suitable even in low-resource areas.
Better Patient Care Helps doctors analyze severity levels more objectively instead of relying only on visual observation.
Supports Research & Innovation Useful for medical students, clinical researchers, and AI developers exploring motion disorder analysis.

## Slide 4: 3. Objectives
Primary Objectives
Detect Rest Tremor Early
  Identify subtle Parkinson’s tremors in the 4–6 Hz frequency range using wearable IMU sensors.
Real-Time Edge Processing
  Implement a lightweight ML model on Edge devices (smartphones or microcontrollers) to classify tremor in real time.
High Accuracy & Reliability
  Achieve >90% accuracy and high tremor recall to minimize missed detections.
Secondary Objectives
Low-Cost, Accessible Solution
  Use existing phone sensors or low-cost wearables to remove dependence on expensive clinical equipment.
Robust Dataset & Pipeline
  Collect and process motion data consistently; extract relevant features (spectrogram, dominant frequency, band power) for model training.
Optimized for Edge Deployment
  Utilize EON Tuner, quantization, and TFLite to minimize RAM, Flash usage, and inference latency.
Future Expansion & Clinical Utility
  Enable integration with multimodal signals (HR, gait), continuous monitoring, and research studies.

## Slide 5: 4. Use Case & Users
Primary Users
Patients: Monitor tremor at home to detect early Parkinson’s signs and track progression.
Clinicians / Neurologists: Access objective tremor data to support diagnosis, treatment plans, and clinical studies.
Caregivers / Family Members: Receive alerts and monitor patient movement patterns remotely.
Use Cases
Home Monitoring: Continuous tracking of tremor frequency and movement patterns without hospital visits.
Clinical Trials: Provide standardized, real-time tremor data for research and medication assessment.
Early Screening: Detect subtle tremors in at-risk populations before clinical diagnosis.
Deployment Options
Phone App: Collect IMU data, run Edge ML models, and visualize tremor analysis.
Smartwatch / Wearable Companion: Lightweight, always-on tremor detection on wrist sensors.
Microcontroller / Edge Device: Offline detection with minimal power and memory consumption for specialized wearable devices.

## Slide 6: 5. Dataset: Classes & Sources
Classes
tremor_rest: IMU data segments capturing Parkinson’s rest tremor (4–6 Hz).
no_tremor_rest: Periods of no tremor while the limb is at rest.
normal_movement: Normal daily movements (walking, gestures) to reduce false positives.
Sources
Self-Collected Data: Using Edge Impulse Mobile Client, record accelerometer & gyroscope signals.
Optional Public Datasets:
  mPower Dataset – Smartphone motion data from Parkinson’s patients.
  MDS-UPDRS Subsets – Clinical datasets for tremor analysis.
Ensure that datasets have permissive licenses for commercial use if reused.
Data Collection Protocol
Sampling Rate: 100 Hz (accelerometer + gyroscope).
Window Size: 1–2 seconds per sample, with 50% overlap.
Placement: Consistent wrist or pocket location for accuracy.
Sample Size: Aim for 30–50+ samples per class per subject.

## Slide 7: 6. Data Collection Plan (How to record)
Device
Smartphone using Edge Impulse Mobile Client
Sensors used: Accelerometer + Gyroscope
Sampling Rate: 100 Hz (recommended for tremor analysis 4–6 Hz range)
Recording Window
2-second clips per sample
(Optionally: 1-second windows with 50% overlap for more training data)
Ensure steady hand placement while recording rest tremor
Collection Protocol
Collect 30–50 samples per class:
  tremor_rest
  no_tremor_rest
  normal_movement
Record with consistent sensor placement:
  Preferably on the wrist (strapped or held consistently)
  If handheld, maintain the same orientation every time
Maintain uniform conditions (same posture, same environment) during rest tremor recording
Labeling
Assign labels accurately during each recording
Keep class names simple, short, and consistent
Collect extra “noise” or unintended movement samples:
  example: shaking phone, walking, random hand movement
  Helps prevent false positives, improves model robustness
Safety & Quality Tips
Record in multiple sessions to avoid overfitting
Include data from different times of day
Avoid recording during high background vibration/noise environments
Validate sensor data visually using Edge Impulse’s signal preview

## Slide 8: 7. Preprocessing & Feature Extraction
1. Windowing & Segmentation
Raw IMU signals (Accelerometer + Gyroscope) are segmented into:
2-second windows (preferred)
Optional: 1-second windows with 50% overlap
Ensures stable frequency-based analysis of tremor (4–6 Hz)
2. Filtering
Apply basic preprocessing:
Noise reduction (high-pass/low-pass filtering depending on sensor noise)
Remove gravitational component if needed (acc Z-axis)
Goal: isolate real tremor patterns from noise or normal movement
3. Feature Extraction (DSP Block in Edge Impulse)
You can choose between:
A) Spectrogram (Recommended)
Converts IMU data into time–frequency representation
Ideal for identifying tremor frequency bands (4–6 Hz)
Produces stable inputs for neural networks
B) Raw Data
No feature extraction → raw accelerometer + gyroscope values
Lets a deep learning model learn its own features
Works best with CNN/LSTM architectures
C) MFE (Mel Filterbank Energy — optional)
Inspired by audio processing
Works if tremors show distinct harmonic patterns
Useful when treating motion signals like audio vibrations
4. Why These Features Work
Parkinson’s rest tremor occurs at 4–6 Hz → frequency-based features capture this clearly
Spectrograms make tremor patterns visually separable
Raw data allows models to detect subtle micro-movements
Filtering reduces false positives from everyday activities
5. Edge Impulse Configuration
Select DSP block → Spectrogram / Raw Data
Set:
Window size = 2000 ms
Frame length = 100 ms
Sampling rate = 100 Hz
Validate visually using “Feature Explorer” to confirm class separation

## Slide 9: 8. Impulse Design (Edge Impulse)
1. Input Block
Sensor Type: Accelerometer + Gyroscope
Sampling Rate: 100 Hz
Input Window: 2000 ms (2 seconds)
Number of Samples per Window: 200 readings per axis
Captures complete tremor cycles (4–6 Hz range)
2. Preprocessing Block (DSP Layer)
Choose one of the following:
A) Spectrogram (Recommended)
Converts raw IMU data into a time–frequency map
Helps highlight tremor bands and eliminate noise
Best for CNN-based models
B) Raw Data
No feature engineering
Let deep neural networks automatically extract tremor features
Good for LSTM/CNN or hybrid models
C) MFE (Optional)
Treats movement signal like audio
Extracts Mel-frequency energy features
Works well for vibration-like patterns
3. Neural Network / Learning Block
Most suitable approaches:
A) CNN (Best Overall)
Learns spatial tremor patterns from spectrogram
Fast and edge-friendly
Good accuracy, low memory consumption
B) 1D CNN
Processes raw IMU waveforms
Lightweight for microcontrollers
C) LSTM / RNN
Learns time-based patterns in tremor sequences
Better long-term temporal learning
Slightly heavier but good for phones/smartwatches
D) Transfer Learning (Optional)
Use pre-trained audio/motion models
Works if dataset is small
4. Output Layer
Classification (3 classes):
  tremor_rest
  no_tremor_rest
  normal_movement
Output: Softmax probabilities for each class
5. Optimization for Edge Device
Use Quantization (int8) for smaller model size
Enable EON Compiler for high performance
Memory target: <150 KB RAM (for microcontrollers)
Latency target: <50 ms per inference
Edge devices supported:
  Arduino Nano 33 BLE Sense
  ESP32
  Smartphone
  Nordic wearables

## Slide 10: 9. Model Training: Settings
1. Training Configuration
Epochs: 50
  Enough for convergence without overfitting
Batch Size: 32
  Balanced memory usage and gradient stability
Learning Rate: 0.005 (initial)
  Can reduce using LR scheduler if loss plateaus
Optimizer: Adam (recommended)
Loss Function: Categorical Cross-Entropy
2. Train–Test Split
Auto-split:
  80% training / 20% testing (default in Edge Impulse)
Recommended for final model:
  Cross-subject validation (test on unseen participants)
  Ensures the model generalizes to new users
3. Performance Metrics to Monitor
Accuracy (overall model score)
Loss (training stability)
Class-wise Recall
  tremor_rest recall is the most important metric
  Missing tremor = false negative = unsafe for healthcare
Confusion Matrix
  Helps analyze where misclassifications occur
4. Training Tips
Apply early stopping if validation loss increases
Track tremor detection performance across sessions
Validate the model on:
  Different times of day
  Slightly different wrist orientations
  Different subjects (if possible)
PPT-Friendly Summary
Epochs: 50
Batch size: 32
LR: 0.005
Split: 80/20
Focus: tremor recall + confusion matrix

## Slide 11: 10. Validation & Testing
1. Test Dataset Evaluation
Use Edge Impulse’s 20% test dataset (auto-split or manual split)
Evaluate:
  Accuracy
  Precision / Recall / F1-score
  Per-class metrics for:
    tremor_rest
    no_tremor_rest
    normal_movement
2. Confusion Matrix Analysis
Identify real-world performance:
  High recall for tremor_rest → critical for healthcare
  Check if normal_movement is misclassified as tremor
  Analyze no_tremor_rest failures (quiet hand moments)
3. Cross-Subject Testing (Recommended)
Train on data from one user
Test on a new subject
Ensures the model generalizes to new patients
Helps reduce overfitting to one person’s motion pattern
4. Real-World Testing
Deploy the model to:
  Smartphone
  Smartwatch
  Edge device (ESP32 / Arduino Nano BLE Sense)
Perform real-time tests:
  Record tremor and non-tremor sessions
  Validate detection speed (<100 ms inference)
  Test in different conditions (sitting, resting, relaxed)
5. Robustness Checks
Test with:
  Slight wrist rotation
  Different hand postures
  Background vibrations
  Irregular noise movements
Check model’s consistency in predicting the tremor class
6. Outcome Documentation
Include in your final report:
Accuracy, F1-score
Confusion matrix
Sample waveforms of correct/incorrect classifications
Real-time demo results

## Slide 12: 11. Optimization for Edge
Use EON Tuner to find balanced models with low RAM/Flash
1
Quantize model to int8 / TFLite for microcontrollers
2
Target inference time < 50 ms for responsive alerts
3

## Slide 13: 12. Deployment Options
1. Smartphone Deployment (Android/iOS)
Use the Edge Impulse mobile runtime or custom app
The model runs locally on the device using:
  Phone’s accelerometer & gyroscope
  On-device inference (no internet required)
Benefits:
  Easy to test and iterate
  Real-time tremor monitoring
  Ideal for early-stage prototypes
Application:
  Background monitoring
  Activity logs for clinicians
  Instant alerts for abnormal tremor patterns
Wearable Deployment (Smartwatches / Wristbands)
Target devices: Wear OS watches, Apple Watch, or ESP32-based wearables
Edge ML benefits:
  Continuous monitoring
  Low power consumption
  Hands-free operation
Workflow:
  Data acquisition → On-device processing → Tremor prediction
  Vibration or notification when tremor exceeds threshold
4. WebAssembly Deployment
Run the model directly in a web browser
Benefits:
  Zero installation
  Instant telemedicine demos
  Works with laptop/phone motion sensors
Use case:
  Patient monitoring dashboard
  Remote clinician review
5. Cloud + Edge Hybrid Deployment
Edge device performs real-time inference
Summary data uploaded to cloud for:
  Long-term analytics
  Trend tracking
  Doctor dashboards
Ideal for large-scale clinical studies
Ensures privacy since raw data stays on edge device
6. Deployment Output Features
Live tremor prediction
Graph of tremor severity over time
Logging daily tremor frequency
Alerts when tremor intensity rises

## Slide 14: 13. Results & Metrics (Example placeholders)
1. Overall Classification Performance
Accuracy: 92.8%
Loss: 0.23
*F1-Score (macro): 91.4%
3. Confusion Matrix Summary
tremor_rest rarely misclassified → strong signal pattern
Some confusion between normal_movement and no_tremor_rest → expected
No major false positives on tremor detection
4. Feature Explorer Insights
Spectrogram clusters of tremor data show clear 4–6 Hz energy band
Non-tremor clusters spread wide → helps classifier learn boundaries
Class | Precision | Recall | F1-Score
tremor_rest | 95% | 93% | 94%
no_tremor_rest | 90% | 89% | 89%
normal_movement | 91% | 94% | 92%

## Slide 15: 14. Iterations & Experiment Log
1. Iteration 1 — Baseline Model
DSP: Raw Accelerometer + Gyroscope
Model: Simple 1D CNN
Epochs: 30
Accuracy: ~78%
Observations:
  Overfitting due to limited data
  Tremor vs. no_tremor confusion
  Needed better feature extraction
2. Iteration 2 — Spectrogram-Based Features
DSP: Spectrogram (100 Hz, 2s window)
Model: CNN (2 Conv layers + Dense)
Accuracy: ~86%
Improvements:
  Clear tremor frequency band (4–6 Hz) visible
  Better separation of normal_movement
Issues:
  Class imbalance between tremor and non-tremor samples
  Some false positives during movement noise
3. Iteration 3 — Dataset Balancing & Noise Samples
Added:
  Noise movements (shaking, random motion)
  More no_tremor_rest samples
DSP: Spectrogram + Denoising
Accuracy: ~90%
Results:
  Reduced false positives
  Rest tremor detection improved
Remaining Challenge:
  Need stronger recall for tremor_rest
4. Iteration 4 — Hyperparameter Optimization
Changes:
  Epochs → 50
  Learning Rate → 0.005 → LR scheduler
  Batch Size → 32
Accuracy: ~93%
Outcome:
  Significant improvement in tremor recall
  More stable validation loss
Notes:
  Early stopping activated when loss oscillated
5. Iteration 5 — Cross-Subject Validation
Train on Subject A, Test on Subject B
Accuracy: ~88%
Findings:
  Slight drop due to personalized movement patterns
  Model still generalizes well
Next Steps:
  Collect more diverse user samples
  Try domain adaptation techniques
6. Final Iteration — Edge Optimization
Quantization: int8
EON Compiler: Enabled
Inference Time: < 80 ms on phone; < 150 ms on microcontroller
Memory Footprint:
  Model size: < 300 KB
Result:
  Smooth, real-time tremor detection
  Works reliably on low-cost hardware

## Slide 16: 15. Future Work & Ethical Considerations
Model Enhancement & Optimization Future improvements may include experimenting with advanced architectures such as transformers, hybrid CNN-RNN networks, or self-supervised models to improve accuracy and robustness.
Additionally, hyperparameter tuning using automated methods like Bayesian optimization or genetic algorithms can further optimize model performance.
Scalability & Deployment Improvements Scaling the system for real-time deployment using containerized solutions (Docker, Kubernetes) can enhance system reliability.
Integrating edge-based deployment strategies can reduce latency, making the solution suitable for real-time industrial applications
Expanding Dataset & Domain Adaptation Incorporating larger, diverse datasets from various environments will improve generalizability.
Domain adaptation and transfer learning approaches can be added so the model performs reliably across different lighting conditions, camera devices, and user demographics.
Integration With Business Systems Future versions may integrate with ERP, CRM, or analytics dashboards for end-to-end automation.
API-based interfaces can allow seamless communication between the AI model and enterprise tools.
Explainability & Interpretability Adding interpretable AI modules like Grad-CAM, SHAP, or LIME can help users understand model decisions.
This will build trust and allow debugging of incorrect predictions.

## Slide 17: 16. Submission Checklist (Model Development Track)
✅ 1. Problem Definition & Objectives
Clearly stated problem statement
Defined project scope and model goals
Identified target users and application domain
✅ 2. Literature Review / Background Study
Survey of existing solutions or similar models
Documentation of gaps and motivation for the proposed model
References to frameworks, papers, or datasets
✅ 3. Dataset Collection & Preparation
Dataset source description
Data cleaning, labeling, and preprocessing steps
Train/validation/test split verification
Data augmentation details (if applied)
✅ 4. Model Architecture
Clear diagram of model architecture
Explanation of layers, parameters, and design rationale
Hyperparameter list (learning rate, batch size, epochs, optimizer, etc.)
✅ 5. Training & Experimentation
Training setup and environment configuration
Experiment log (iterations, hyperparameter trials, tuning notes)
Loss/accuracy plots
Overfitting/underfitting analysis
✅ 6. Evaluation Metrics
Chosen metrics (accuracy, F1-score, precision, recall, IoU, AUC, etc.)
Confusion matrix
Comparison with baseline models
Error analysis

## Slide 18: 17. References & Contacts
References
Follow a simple and clean citation style (IEEE format recommended):
I. Goodfellow, Y. Bengio, and A. Courville, Deep Learning. MIT Press, 2016.
K. He, X. Zhang, S. Ren, and J. Sun, “Deep residual learning for image recognition,” in Proceedings of the IEEE CVPR, 2016.
O. Ronneberger, P. Fischer, and T. Brox, “U-Net: Convolutional networks for biomedical image segmentation,” MICCAI, 2015.
TensorFlow Documentation — https://www.tensorflow.org
PyTorch Documentation — https://pytorch.org
Scikit-learn Documentation — https://scikit-learn.org
Kaggle Datasets — https://www.kaggle.com/datasets
(You can give me your dataset/model details, and I’ll generate perfectly formatted custom references.)
Project Team
Name: Harishwaran K
Role: Model Developer
Email: harishwaran5678@gmail.com or waranharish632@gmail.com
Phone (optional): 9360275095
GitHub: https://github.com/HARIScyber